## Slide 1: EEG analysis overview

## Slide 2
Install EEGLAB toolbox (you can Google it to download the files).
Run eeglab in MATLAB.
Load the raw data (entrain_NAP_###_1.bdf).
  File – Import Data – Using EEGLAB functions and plugins – From Biosemi BDF file
  Assign references, 35 and 36 (bilateral mastoids; this is necessary for a Biosemi file)
As this is a huge file and you only need the entrainment task portion, trim the data. To figure out when the entrainment task starts and ends, look at time stamps for events.
  Edit – Select data
  In an appropriate box, put the time range
Apply a bandpass filter.
  Tools – Filter the data Basic FIR filter (new, default)
  Lower limit: about 0.1 Hz, Upper limit: about 20-30 Hz
  The length of order should be long enough.
  This may take really long time.

## Slide 3
Assign channel locations
  Edit -> Channel locations
  Add coordinates using the file at https://www.biosemi.com/download/Cap_coords_all.xls
Down-sample data if necessary
  Tools -> Change sampling rate
Run a component analysis
  There is a built-in ICA tool, but I recommend installing AMICA (adaptive mixture of ICA), downloadable below
  https://sccn.ucsd.edu/~jason/amica_web.html
  Once the installation is completed, you can run it as if this is a built-in function in EEGLAB

## Slide 4
  For more information, please see below:
    https://sccn.ucsd.edu/~jason/amica_help.html
    https://sccn.ucsd.edu/wiki/AMICA
  To maximize the performance, it is very important to eliminate occasional artifacts and noise in your original data set before running AMICA.
Extract epochs
  Tools -> Extract epochs
  Set an appropriate time window and a baseline
Reject bad components or epochs
  There are various ways to reject components and epochs.
  I typically reject components by visual inspection in order to delete eye blink and eye movement artifacts.
  To reject epochs, I typically delete epochs that exceed a max. magnitude.

## Slide 5
Plot data
  EEGLAB provides many types of figures, although I would use my own codes for publication.
  My favorite plot is:
    Plot -> Channel ERPs -> with scalps maps